## Slide 1: Final Year Project : Studying the effects of vision on balance

## Slide 2: The hypothesis:
Affecting visual stimuli when a person sways, such that the sway of the stimuli is different from expected, should result in the person having difficulty to balancing.
Excessively affecting visual stimuli however, will have less or no effect on the person’s ability to balance

## Slide 3: The core approach
Create a Virtual Reality Environment
Measure the sway of a user in real time
Manipulate the Virtual Reality Environment so that the visual input sways more than user is swaying

## Slide 4: Measuring Sway
Force Plate
  Measures centre of pressure
  Can use a low pass filter to estimate centre of mass as well
Head set position
  Measures centre of mass

## Slide 5: Wiiboard Justification
Accuracy of force and center of pressure measures of the Wii Balance Board
Validity and reliability of the Nintendo Wii Fit Stillness score for assessment of standing balance
Validity of the Nintendo Wii® balance board for the assessment of standing balance in Parkinson’s disease
Comparison of a laboratory grade force platform with a Nintendo Wii Balance Board on measurement of postural control in single-leg stance balance tasks

## Slide 6: Wiiboard latency problem

## Slide 7: Wiiboard connection problem
No solutions available to create a class in Unity to connect with my wiiboard
Either have to create a 3rd party software that communicates with Unity or create my own Wiimote C library
Local UDP Socket has 0.2ms latency

## Slide 8: Key technologies
UDP Socket with Wiimote Library
Unity project scene
Pimax Virtual reality headset
Wiiboard
Bluetooth
C# UDP Socket
UDP Socket
Python script
Matplotlib
Unity scripts
SteamVR Unity package
PiTool
XR Interaction toolkit + OpenVR

## Slide 9: Key technologies
UDP Socket with Wiimote Library
Unity project scene
Pimax Virtual reality headset
Wiiboard
Bluetooth
C# UDP Socket
UDP Socket
Python script
Matplotlib
Unity scripts
SteamVR Unity package
PiTool
XR Interaction toolkit + OpenVR

## Slide 10: Choice of stimulus

## Slide 11: Various Approaches to the Sway Problem
Moving the stimuli

## Slide 12: What I learned
Choice of inputs – only need head input
Choice of stimuli – most of the information is not in FOV
Choice of motion, no angular motion and no parallax effect

## Slide 13: Choice of stimulus

## Slide 14: Various Approaches to the Sway Problem
Inverse pendulum camera

## Slide 15: Various Approaches to the Sway Problem
2 parts:
Rotation
Get change in orientation of real – world input
Apply sensitivity
Apply to Simulated camera’s previous rotation
Position
Get Vector of displacement of real – world input
Apply inverse of real – world rotation
Apply Simulated camera’s rotation
Apply sensitivity
Apply to Simulated camera’s position
Changing camera based on VR headset orientation and position change

## Slide 16: Demo!

## Slide 17: Experiments
Each participant has 30s of “Control”, 60s of “Test” and 20s of “Aftermath”
Blue balance foam to slightly off balance user
Sensitivity settings: -0.5, 0.5, 1, 1.5, 1.75, 2
Each participant is asked to idly move their head
Order of sensitivity is different for every participant

## Slide 18: Experiments Results + analysis

## Slide 19: Experiments Results + analysis

## Slide 20: Conclusion & Evaluation
Looks like there is a trend that supports the first part of the hypothesis
The experiments need to be tuned more – the users noted if they try particularly hard to balance or if they do not move their head it is quite easy to not get unbalanced
A key goal was to make solid documentation and legible code in order to allow this work to be continued